## Slide 1
Project: Fanuc Olympiads
Presentation of the sequence 5: activities and a pre-project analysis
CARVALHO BÜRGER Karoline
DE JESUS RODRIGUES Tiago
ELLER CRUZ Rafael
NOGUEIRA Rafael Accacio

## Slide 2
Summary:
1 – Performed activities;
2 – Project management: principles and choices;
3 – Pre-project analysis;
3.1 – Problem presentation;
3.2 – Proposed Solutions;
3.2.1 – Robots choice;
3.2.2 – Robots positioning;
3.2.3 – Robots movements;
3.2.4 – Simulation issues;
4 – Conclusion.

## Slide 3
1 – Performed activities

## Slide 5
2 – Project management: principles and choices

## Slide 7
Objectives: What must be achieved
Constraints: Context and limitations

## Slide 8
Solution: A functioning simulation

## Slide 9
Validation: Checking that the simulation fulfills the objectives

## Slide 10
Follow up and Optimization: Criticizing and proposing better solutions (time, cost, space, energy consuption)

## Slide 11
Final Project: Description, consolidation and argumentation

## Slide 12
3 – Pre-project analysis

## Slide 13
3.1 – Problem presentation

## Slide 14
3.2 – Proposed solution
We can divide the proposed solution analysis in four steps:
Robots choice;
Robots positioning;
Robots movements;
Simulation issues.

## Slide 15
3.2.1 – Robots choice
Project specifications:
- Load at wrist: 25.8 kg
- Minimum reach: 2075 mm
Robot chosen: R-2000iB/100H
- Maximum load capacity at wrist: 100 kg
- Maximum reach: 2655 mm
- Mechanical weight: 1150 kg
- Axis: 5
Robot palletizer series:
- M-710iC
- R-1000iA
- R-2000iB
- M-410
Palletizer robot:

## Slide 16
Bottle robot:
3.2.1 – Robots choice
Project specifications:
- Load at wrist: 5.74 kg
- Minimum reach: 414 mm
Robot chosen: LR Mate 200iD/7L
- Maximum load capacity at wrist: 7 kg
- Maximum reach: 911 mm
- Mechanical weight: 27 kg
- Axis: 6
LR Mate serie:
- LR Mate 200iD/7LC

## Slide 17
3.2.1 – Robots choice
Palletizer robot:
By simulation:
- 12.5s two boxes are filled
- Round-off trip in 5.55s
Conclusion:
- It’s possible for the palletizer robot chosen
Bottle robot:
Especification:
- 1.75s for 8 bottles
By simulation:
- Robot takes 2.5s for 4 bottles
Conclusion:
- It’s necessary two bottle robots

## Slide 18
3.2.2 – Robots positioning
Bottle robots:
Box conveyor height: 1085 mm
Robot’s maximum reach: 911 mm
Pedestal is needed!
Chosen height: 1100 mm
Furthest drop-off horizontal distance: 509.5 mm
Horizontal distance from the conveyor: 335 mm
Palletizing robot:
Boxes stack height: 3023.5 mm
Robot’s maximum reach : 2655 mm
Pedestal is needed!
Chosen height: 1400 mm
Horizontal placement: equidistant from boxes and pallets conveyors

## Slide 19
3.2.3 – Robots movements

## Slide 20
600 mm
3.2.3 – Robots movements

## Slide 21
3.2.4 – Simulation issues
Controller
DCS
DCS

## Slide 22
4 – Conclusion

## Slide 24
Thank you for your attention!

## Slide 25
Any question?